## Slide 1
PIPELINE CPU PROJECT · FINAL DEMO
A 5-stage RISC-V RV32I processor in Verilog
46 encodings, full forwarding, a load-use interlock, branch prediction, and machine-mode interrupts. Verified byte-for-byte against a golden reference model we wrote ourselves, and synthesized for an Artix-7 at 74 MHz.
IF
ID
EX
MEM
WB
bypass network
interlock / stall
flush / killed
free
DESIGN
杨辉宗 1820232064 · microarchitecture, hazard scheme, design document
CODING
吴宏庆 1820232044 · 19 RTL modules, assembler, reference model
TESTING
王伟成 1820232061 · testbenches, trace diffing, performance measurement

## Slide 2
THE MACHINE
One 5-stage pipeline, 46 encodings, two bonuses
IF
ID
EX
MEM
WB
STAGE RESPONSIBILITIES
IF
Fetch from IMEM; BHT lookup indexed by the fetch PC
ID
Decode, immediate generation, register read; jal resolved here (1 bubble)
EX
ALU, branch compare + target, forwarding muxes; branches + jalr resolve here (2 bubbles)
MEM
Data memory load/store; the BRAM word is registered on the MEM edge
WB
Byte-lane select + extension, then register write-back
46
encodings
37 core + 9 system
2
bonus features
BHT + interrupts
INSTRUCTION SET
R-TYPE
add sub sll slt sltu xor srl sra or and
I-ARITH
addi slti sltiu xori ori andi slli srli srai
LOADS/STORES
lb lh lw lbu lhu · sb sh sw
BRANCHES
beq bne blt bge bltu bgeu
U + JUMPS
lui auipc jal jalr
SYSTEM
ecall ebreak csr* mret
The shallowest design that still exposes all three hazard classes — which is the point of the exercise.

## Slide 3
HAZARDS
Three mechanisms, one rule each
FORWARD
EX/MEM and MEM/WB results route straight back to the ALU inputs — no stall for a data hazard.
EX/MEM wins over MEM/WB · x0 never forwarded · store data forwarded too
STALL
A load feeding the very next instruction is the one case forwarding cannot save.
load-use interlock · freeze PC + IF/ID · one bubble into ID/EX
FLUSH
A taken branch or trap squashes the younger instructions already in the pipe.
jal = 1 bubble · branch / jalr / trap / mret = 2 bubbles · killed insns never retire
Everything above CPI 1.0 is control-flow bubbles and load-use stalls. There is no other source of delay.

## Slide 4
DEMO
The machine in simulation
pc_q · stall · flush_id · fwd_a — the three hazards, live
WHAT TO POINT AT
STALL
stall high for exactly one cycle; PC and IF/ID hold their value
FORWARD
fwd_a switches to the MEM/WB path the cycle after the stall
FLUSH
both flush signals assert; the trace valid never fires for a killed insn
Function is shown in simulation, not asserted — every test states its own PASS or FAIL verdict.

## Slide 5
VERIFICATION
Green against an independent model, not our own expectations
RESULTS — ALL FOUR FORWARDING × BHT CONFIGURATIONS
Per-instruction
one program per encoding, golden state
46 / 46
Hazard
forwarding, load-use, flush, CSR
9 / 9
Program-level
fib, bsort, bloop, bpred, irq — trace diff vs ISS
5 / 5
Unit testbenches
imm_gen, ALU, regfile, control, BHT…
11 / 11
Toolchain self-check
assembler vs reference model
4,323
WHY A TRACE DIFF
A final-state check tells you the answer is wrong. A commit-trace diff tells you which instruction went wrong — the difference between an afternoon of debugging and a week.
TESTS ARE TRUSTED, NOT JUST PASSING
Every expected value is generated by the reference model, and we injected deliberate bugs to confirm each testbench fails when it should.
Correctness rests on EX-stage resolution + flush — the predictor only changes when instructions are fetched, never what they compute.

## Slide 6
PERFORMANCE
Every figure carries its own baseline
FORWARDING ON VS OFF — SAME PROGRAMS
Program
CPI fwd on
CPI fwd off
Speedup
fib
1.368
2.263
1.65×
bsort
1.376
1.904
1.38×
bloop
1.396
1.707
1.22×
average
1.387
1.837
1.32×
A feature is switched off and the same programs re-run — the 'show performance' requirement, not a number with no baseline.
95.5%
BHT accuracy
branch-heavy demo
−14.5%
cycles saved
same program
THE HONEST PART
A 2-bit table helps loop-dominated code (fib 93.4%), and hurts on alternating branches (49.9%, +10%). We report the case where it loses.
The BHT is a cheap heuristic, not a guarantee — and saying so is more useful than hiding the case where it loses.

## Slide 7
BONUS FEATURES
Two shipped, one deliberately cut
INTERRUPTS — CSRS + MRET
CSRS
mstatus (MIE/MPIE) · mie · mtvec · mepc · mcause
INSNS
csrrw csrrs csrrc + immediate forms · mret
DEMO
testbench-driven irq → timer-like ISR saves regs, toggles a counter, returns via mret
RESULT
21 assertions PASS · 633/633 trace lines match the ISS · irq held while MIE=0
THE TRAP ASYMMETRY
ecall leaves mepc at the ecall itself — the handler adds 4 before mret. An interrupt leaves mepc at an instruction that never ran, so the handler must not. Get this wrong and the handler loops forever.
I-CACHE — DESIGNED, NOT BUILT
Direct-mapped 128 × 16 B (2 KB) — but the whole suite fits in 2 KB, so the hit rate would read ~99% on every program. A figure that reads 99% proves nothing.
Both bonuses are switchable off — a feature that cannot be disabled cannot be measured.

## Slide 8
SYNTHESIS
74 MHz on an Artix-7, with the path that limits it
74 MHz
setup met
13.5 ns · WNS +0.052
1,461
LUTs
post-route
819
flip-flops
post-route
2
BRAMs
IMEM + DMEM
CRITICAL PATH — THE LOAD-TO-BRANCH CHAIN
DMEM block-RAM clock-to-output (2.454 ns, the largest single term) → byte-lane select + sign extension in WB → the MEM/WB→EX forwarding mux → branch comparator → redirect into the PC clock-enable.
A 16-instruction minimum; we shipped 46, verified byte-for-byte, synthesized at 74 MHz — with both bonuses green. Thank you.