## Slide 1
Computer Organization · BIT Y4T1
IF
ID
EX
MEM
WB
PIPELINE CPU PROJECT · MIDTERM REVIEW
A 5-stage RISC-V
RV32I processor in Verilog
46 instruction encodings, full forwarding, a load-use interlock, branch prediction and machine-mode interrupts. Verified against a golden reference model we wrote ourselves, and synthesized for an Artix-7.
IF
ID
EX
MEM
WB
Colours used throughout: bypass network interlock / stall flush / killed free
DESIGN
[ 杨辉宗 ] · microarchitecture, hazard scheme, design document
CODING
[ 吴宏庆 ] · 19 RTL modules, assembler, reference model
TESTING
[ 王伟成 ] · testbenches, trace diffing, performance measurement
What we propose to build, why we chose it, and the prototype that already shows it works.
Notes: Good morning. We're proposing a five-stage pipelined CPU implementing
the RISC-V RV32I instruction set, written in Verilog and verified in
Vivado.
Three of us. I own the design, [name] owns the RTL and the toolchain,
[name] owns verification and measurement.
Point at the coloured blocks. "Those five colours are the pipeline stages and
they're used consistently throughout. The three underneath are the bypass
network, the interlock, and a flush."

## Slide 2
01 · Design
IF
ID
EX
MEM
WB
2 / 20
THE TASK
What we are building, and how it will be judged
THE COURSE TASK, VERBATIM
"Design a pipeline CPU based on MIPS/RISC-V or other instruction subsets with more than 16 instructions. And implement the CPU by Verilog HDL. Use the simulation tools to show the function and performance of your CPU."
"Bonus items: support interrupt, cache, branch prediction."
EXPLICITLY OUT OF SCOPE
No FPGA board bring-up. The task says simulation tools, so we deliver simulation plus a synthesis report on a named part. No instruction cache; the reasoning is on the next slide.
WHAT WE COMMIT TO DELIVER
MACHINE
A 5-stage in-order RV32I pipeline, 46 encodings, full forwarding, load-use interlock, flush-based recovery
BONUS x2
A 2-bit branch predictor and machine-mode interrupts, each measurable and each switchable off
TOOLCHAIN
An assembler and an independent reference model, because the named tool cannot execute this ISA
EVIDENCE
A self-checking test suite, a design document, and a synthesis report for xc7a35tcpg236-1
HOW WE WILL KNOW IT IS DONE
CORRECT
Every instruction checked against an independent implementation, byte for byte
FUNCTION
Shown in simulation, every test stating its own PASS or FAIL verdict
PERFORMANCE
Measured by switching a feature off and re-running. A number with no baseline proves nothing
SYNTHESIS
An fmax and a utilisation figure on a named part, with the critical path identified
We are past proposing this on paper. A working prototype already meets every criterion above, and the rest of this talk is the evidence.
Notes: Here's the task, verbatim. Design a pipelined CPU with more than
sixteen instructions, implement it in Verilog HDL, and use the
simulation tools to show its function and its performance. Bonus marks
for interrupts, cache and branch prediction.
What we commit to deliver is on the top right. A five-stage in-order
RV32I pipeline with forty-six encodings, full forwarding, a load-use
interlock and flush-based recovery. Two of the three bonuses — branch
prediction and interrupts — each built so it can be switched off,
because a feature you can't disable is a feature you can't measure. An
assembler and an independent reference model, because the tool the
brief names cannot execute this instruction set. And the evidence: a
self-checking test suite, a design document, and a synthesis report on
a named part.
Below that is how we'll know it's done. Four criteria. Correctness
checked against an independent implementation, not against our own
expectations. Function shown in simulation, with every test stating
its own pass or fail. Performance measured by switching a feature off
and re-running the same programs — a number with no baseline proves
nothing. And an fmax and utilisation figure with the critical path
identified.
Two things are explicitly out of scope. No FPGA board, because the
brief asks for simulation. And no instruction cache — the next slide
but one says why.
[RIGHT] And I should be straight with you about where this proposal
stands. We're past proposing it on paper. A working prototype already
meets every criterion on this slide, and the rest of the talk is the
evidence.

## Slide 3
01 · Design
IF
ID
EX
MEM
WB
3 / 20
SPEAKER 1 OF 3 · [ 杨辉宗 ]
Design — the specification the RTL was written against
Every decision below was made and written down before a line of Verilog existed, so the coder implemented a specification rather than inventing one.
OWNED END TO END
MICROARCH
Five-stage structure, pipeline-register fields, PC-select priority
ISA
Instruction subset, all six formats, immediate extraction, CSR zimm
HAZARDS
Forwarding rules and priority, load-use interlock, flush rules
MEMORY
Harvard layout, sizes, byte lanes, misalignment policy, reset
TRAPS
CSR set, mepc / mcause, the ecall versus interrupt asymmetry
REVIEW
Read every RTL module against the spec before it was committed
46
encodings specified
37 core + 9 system
22
control signals
per instruction
1,819
lines of spec
the living document
DELIVERED
• The 46-encoding ISA table and all six immediate formats
• The 46-row control truth table, 22 signals wide
• CSR, trap and mret semantics; docs/DESIGN.md kept current
WHERE TO LOOK
docs/DESIGN.md. The control truth table is generated from the same source that generates the decoder's test vectors, so document and test cannot drift apart.
The design document is not a write-up of what was built. It is what the build was checked against.
Notes: My job was to produce the specification the RTL was written against,
before any Verilog existed.
Six areas. The five-stage structure and what every pipeline register
carries. The instruction subset and all six immediate formats. The
hazard rules — what forwards, what stalls, what gets flushed. The
memory subsystem, sizes, byte lanes and reset. The trap semantics. And
reading every RTL module against the spec before it was committed.
The number I'd point to is the control truth table: forty-six
instructions, twenty-two control signals each. It's in the design
document, and it's GENERATED from the same source that generates the
decoder's simulation vectors. So the document and the test cannot
drift apart. Change the decode and both move together, or the build
fails.

## Slide 4
01 · Design
IF
ID
EX
MEM
WB
4 / 20
SCOPE
46 encodings against a 16-instruction requirement
COURSE MINIMUM
16
IMPLEMENTED
46
2.9× the requirement
R-TYPE
10
add sub sll slt sltu
xor srl sra or and
I-ARITHMETIC
9
addi slti sltiu xori ori
andi slli srli srai
LOADS
5
lb lh lw lbu lhu
sign / zero extended
STORES
3
sb sh sw
byte-lane writes
BRANCHES
6
beq bne blt bge
bltu bgeu
U-TYPE & JUMPS
4
lui auipc
jal jalr
SYSTEM — THE INTERRUPT BONUS
9
csrrw csrrs csrrc csrrwi csrrsi csrrci
ecall ebreak mret
All 46 follow the RISC-V Unprivileged and Privileged specifications exactly. fence and wfi decode as illegal.
ebreak doubles as the simulation halt. RV32I has no halt instruction, so it raises a done flag the testbench watches.
Notes: The brief asks for more than sixteen instructions. We implement forty-
six encodings: thirty-seven core RV32I plus nine system instructions.
[RIGHT] Ten register-register operations, nine immediate arithmetic,
five loads, three stores, six branches, two upper-immediate, two
jumps. Then the nine system encodings — the six CSR instructions,
ecall, ebreak and mret. Those exist because of the interrupt bonus.
One detail: RV32I has no halt instruction, so we use ebreak as the
simulation halt. When it retires it raises a done flag and the
testbench stops.

## Slide 5
01 · Design
IF
ID
EX
MEM
WB
5 / 20
DESIGN CHOICES
What we chose, and what we ruled out
Decision
We chose
Instead of
Why
ISA
RISC-V RV32I, 46 encodings
MIPS
A clean orthogonal encoding we could assemble and model ourselves, and 2.9x the 16-instruction minimum
Pipeline
5-stage in-order
Single-cycle, or a deeper pipe
The shallowest design that still exposes all three hazard classes, which is the point of the exercise
Branches
jal in ID, branches and jalr in EX
Everything in one stage
jal needs no register, so resolving it early is free. Branches need a compare, and doing it in EX keeps it off the decode path
Bonus A
2-bit branch history table
Static prediction only
Cheap in area, and its accuracy is a number we can report honestly, including where it loses
Bonus B
CSRs, traps and mret
--
Exercises privileged state and trap semantics, demonstrable from a testbench-driven interrupt line
Bonus C
Instruction cache - CUT
Building it anyway
Behind a single-cycle memory a hit and a miss cost the same, so CPI would not move, and the suite fits in 2 KB so the hit rate reads ~99 %. Designed and written up, not built.
Reference
Our own Python model
Mars4_5, as the brief names
Mars executes MIPS. It cannot assemble or check RISC-V, so there was no oracle to borrow
Target
Simulation + synthesis report
FPGA board demo
The brief asks for simulation. Synthesis still yields fmax and utilisation without board bring-up risk
The cache was cut on a measurement argument, not a schedule one. A figure that reads 99 % on every program says nothing about the design.
Notes: Eight decisions, each shown with the alternative we rejected.
RISC-V rather than MIPS, because it's a clean orthogonal encoding we
could write our own assembler and reference model for.
Five stages rather than single-cycle or something deeper, because it's
the shallowest design that still exposes all three hazard classes.
That's the point of the exercise.
jal resolved in decode and branches in execute, rather than everything
in one stage. jal needs no register value, so resolving it early costs
nothing. A branch needs a comparison, and doing that in execute keeps
it off the decode path.
The two bonuses we took are both cheap in area and both produce a
number we can report.
[RIGHT] And the one we cut, which is the highlighted row. An
instruction cache sitting behind a single-cycle memory would make a
hit and a miss cost exactly the same, so CPI would not move at all.
And our entire test suite fits in two kilobytes, so the hit rate would
read about ninety-nine percent on every program we ran. It's designed
and written up in the report. We didn't build it, and that was a
measurement argument, not a schedule one.
Last two rows: our own reference model, because Mars executes MIPS and
cannot check RISC-V. And simulation plus a synthesis report rather
than a board, because the brief asks for simulation and synthesis
still gives us fmax without board bring-up risk.

## Slide 6
01 · Design
IF
ID
EX
MEM
WB
6 / 20
DATAPATH
Five stages, three bypasses, one interlock
IF
pc.v + PC-select mux
imem.v 4 KB sync read
bht.v lookup
ID
control.v · alu_ctrl.v
regfile.v read
imm_gen.v 6 formats
EX
forward mux A / B / C
alu.v 11 operations
branch_unit.v · csr.v
MEM
dmem.v 4 KB
byte-lane select
WB
lane extend + wb mux
regfile write (x0 dropped)
commit trace port
IF/ID
ID/EX
EX/MEM
MEM/WB
EX/MEM → EX distance 1 priority
MEM/WB → EX distance 2
carries load data
jal target — ID, 1 bubble
branch · jalr · mtvec · mepc — EX, 2 bubbles
load-use interlock — hold PC and IF/ID, bubble ID/EX
Every stage boundary is an explicit register with stall and flush inputs, so the hazard logic plugs in without touching the datapath.
Notes: Four builds. This is the architecture slide — do not rush it.
This is the datapath we're proposing. Let me build it up.
[STEP 1] Five stages. Fetch reads instruction memory and looks up the
branch predictor. Decode runs the control unit, generates the
immediate and reads the register file. Execute has the ALU, the branch
comparator and the CSR file. Memory is the data memory. Write-back
extends the load, picks the result and writes the register file.
[RIGHT] Between every pair of stages is an explicit pipeline register,
each with a stall input and a flush input. That matters, because it
means the hazard logic plugs in without modifying the datapath at all.
[RIGHT] Two forwarding paths, both landing back in Execute. One from
the Execute-Memory boundary, one instruction ahead. One from Memory-
Writeback, two ahead, and that's the path that carries load data. When
both match, the first wins — [name] will explain why.
[RIGHT] And the redirects. A jal resolves in decode and costs one
bubble. Branches, jalr, traps and mret resolve in execute and cost
two. The dashed violet line is the load-use interlock.
Memory is Harvard — separate four-kilobyte instruction and data arrays
— so fetch and memory access never contend.

## Slide 7
01 · Design
IF
ID
EX
MEM
WB
7 / 20
FEASIBILITY
What already works
Every commitment on the objective slide has been met once already, on a prototype that runs today. The schedule on the next slide is what remains.
BUILT AND RUNNING
DESIGN
Microarchitecture, hazards, memory and the 46-row control truth table, documented
RTL
19 Verilog modules; the machine executes all 46 encodings
BONUS A
Branch predictor, with accuracy and cycle deltas measured
BONUS B
Interrupts. Trap entry, ISR and mret, all diff-tested against the reference model
VERIFICATION
Every suite green at all four build configurations
SYNTHESIS
Placed and routed; setup timing met at 74 MHz on the target part
The specification came first and the implementation followed it. That order is why the schedule on the next slide is credible.
Notes: Briefly, the evidence that this plan is achievable, because it's
already been done once.
Design documented. Nineteen Verilog modules running all forty-six
encodings. Both bonuses working. Every test suite green at all four
build configurations. Placed and routed, with setup timing met at
seventy-four megahertz on the target part.
The specification came first and the implementation followed it. That
order is why the schedule on the next slide is credible rather than
optimistic.

## Slide 8
01 · Design
IF
ID
EX
MEM
WB
8 / 20
DELIVERABLES
What we hand over, who owns it, and when
DELIVERABLES, ONE OWNER EACH
Artefact
Owner
State
Design document and control truth table
Design
complete
19 RTL modules, plain Verilog-2001
Coding
complete
Assembler and reference model
Coding
complete
Self-checking test suite
Testing
complete
Performance measurements
Testing
preliminary
Synthesis report: fmax and utilisation
Testing
one run left
Live demo and script
All three
Sep 16
MILESTONES
SEP 11-12
Apply the two timing improvements; full regression after each
SEP 13-14
Final synthesis run; lock the performance chapter
SEP 15
Feature freeze - bugfix and measurement only
SEP 16
Demo script, waveform captures, rehearsal
SEP 17
Final presentation and demo
RISKS, AND WHAT WE DO ABOUT EACH
TIMING
If the two improvements do not close cleanly by Sep 14, we freeze on the 74 MHz build that is already verified
REGRESSION
One change moves when a load result is available, so it can shift CPI. Figures are re-measured after the freeze
TOOLCHAIN
If Vivado 2019.2 is required, the RTL is plain Verilog-2001 with no IP and a project script is committed
Every deliverable has exactly one owner, and cross-review is by reading each other's work, not by silent edits.
Notes: Seven deliverables, each with exactly one owner and a state.
The design document, the RTL, the assembler and reference model, and
the test suite are complete. Performance measurements are preliminary.
The synthesis report has one run left. The demo lands on the
sixteenth.
Milestones on the right. Timing work on the eleventh and twelfth, with
a full regression after each change. Final synthesis on the thirteenth
and fourteenth. Feature freeze on the fifteenth — bugfix and
measurement only after that. Rehearsal on the sixteenth. Demo on the
seventeenth.
Then three risks, each with what we actually do about it. If the
timing work doesn't close cleanly by the fourteenth, we freeze on the
seventy-four megahertz build that's already verified, rather than ship
something faster we haven't tested. One of those timing changes moves
when a load result becomes available, so it can shift our cycle counts
— which is why every performance figure gets re-measured after the
freeze, not before. And if the instructor requires the older Vivado,
the RTL is plain Verilog-2001 with no vendor IP, and we commit a
project-generation script rather than a version-locked project file.
[RIGHT] Every deliverable has exactly one owner, and cross-review is
by reading each other's work rather than silent edits.
[Name] will take you through the implementation.

## Slide 9
02 · Implementation
IF
ID
EX
MEM
WB
9 / 20
SPEAKER 2 OF 3 · [ 吴宏庆 ]
Coding — the RTL, and the toolchain it needed
The course names Mars4_5 as the simulator, but Mars executes MIPS. Building a RISC-V machine meant building the tools to assemble and check it first.
OWNED END TO END
RTL
All 19 modules: pipeline registers, datapath, hazard logic, CSR file, BHT, counters, memories, top level
ASSEMBLER
Two-pass, six formats, directives and pseudo-ops, emits a $readmemh image
REFERENCE
A second implementation of the ISA in Python, emitting the commit trace
FLOWS
The xsim batch flow and the non-project synthesis flow, both scripted
FIXES
Every failure the tester raised, re-verified by their regression
19
RTL modules
Verilog-2001
861
lines of assembler
asm.py
589
lines of ISS
iss.py
DELIVERED
• 19 synthesizable modules, no vendor IP, no block design
• asm.py and iss.py, cross-validated against each other
• sim/run.sh and vivado/synth.sh, reproducible from the shell
WHERE TO LOOK
rtl/ and tools/. The machine executes all 46 encodings and places and routes at 74 MHz on the target part.
The assembler and the reference model were cross-validated against each other before any RTL existed, so the oracle was trustworthy on day one.
Notes: Thanks. I own all the RTL, and also the toolchain — and the toolchain
is the part that's less obvious, so let me start there.
The brief names Mars as the simulator. Mars executes MIPS. We're
building a RISC-V machine, so Mars cannot assemble our programs and
cannot tell us whether our CPU is right. There was no reference to
check against, so I wrote one.
An assembler, about eight hundred and sixty lines, two passes, all six
instruction formats. And a reference model — an instruction set
simulator in Python, about five hundred and ninety lines, which runs
the same program and prints what every instruction committed.
Those two were cross-validated against each other BEFORE any Verilog
existed. So by the time the RTL needed checking, the oracle was
already trustworthy.

## Slide 10
02 · Implementation
IF
ID
EX
MEM
WB
10 / 20
DATA HAZARDS
Forwarding: two distances, one priority rule
DISTANCE 1 — PRODUCER IS IN MEM
c1
c2
c3
c4
c5
c6
addi x5, x0, 100
IF
ID
EX
MEM
WB
add x6, x5, x5
IF
ID
EX
MEM
WB
fwd = 2'b10
DISTANCE 2 — PRODUCER IS IN WB
c1
c2
c3
c4
c5
c6
addi x5, x0, 100
IF
ID
EX
MEM
WB
nop
IF
ID
EX
MEM
WB
add x6, x5, x5
IF
ID
EX
MEM
fwd = 2'b01
PRIORITY — WHEN BOTH MATCH, EX/MEM WINS
The instruction in MEM is the newer writer, so its value is the one the architecture says you read. Testing MEM/WB first resurrects the stale value.
x5 = 100 then x5 = x5 + 1 then read x5 must see 101, while 100 is still sitting in MEM/WB
A producer whose destination is x0 wrote nothing, so it is never forwarded. Otherwise x0 would read non-zero for exactly one instruction.
Notes: Data hazards. An instruction reads its registers in decode, but the
instructions ahead of it haven't written back yet.
[STEP 1] Distance one: the producer is in memory. Its result already
exists at the Execute-Memory boundary, so we forward it straight into
the ALU input.
[RIGHT] Distance two: the producer is in write-back. That's the
Memory-Writeback path, and it's also the path that carries load data,
which matters in a minute.
There's a third distance handled inside the register file — a write-
to-read internal bypass, so if write-back is writing the register
decode is reading in the same cycle, decode sees the new value.
[RIGHT] And the rule that catches people out. When both older
instructions write the same register, Execute-Memory wins, because
it's the newer writer. Check Memory-Writeback first and you resurrect
a stale value. Our hazard test does exactly that: set x5 to a hundred,
add one, then read it. It must see a hundred and one while a hundred
is still sitting in the older register.
One more: we never forward from x0. A producer whose destination is x0
wrote nothing, so forwarding it would make x0 read non-zero for one
instruction.

## Slide 11
02 · Implementation
IF
ID
EX
MEM
WB
11 / 20
THE TWO HAZARDS FORWARDING CANNOT FIX
One cycle for a load-use, two for a taken branch
LOAD-USE INTERLOCK — 1 STALL CYCLE
c1
c2
c3
c4
c5
c6
c7
lw x7, 0(x5)
IF
ID
EX
MEM
WB
add x8, x7, x0
IF
ID
ID
EX
MEM
WB
sub x9, x8, x1
IF
ID
ID
EX
MEM
violet = held. PC and IF/ID freeze, ID/EX takes a bubble.
One cycle is always enough. By then the load is in WB.
TAKEN BRANCH — 2 BUBBLES
c1
c2
c3
c4
c5
c6
beq (taken)
IF
ID
EX
MEM
WB
branch + 4
IF
ID
X
branch + 8
IF
X
target
IF
ID
EX
resolved here
COST load-use 1 stall jal 1 bubble taken branch 2 jalr 2 ecall / interrupt / mret 2 wrong-path slots never write and never retire
A redirect always overrides a stall: the instruction that raised the stall is being killed anyway, so waiting for it would deadlock the redirect.
Notes: Two hazards forwarding cannot fix.
[STEP 1] A load. Its data doesn't exist until the end of the memory
stage, so an instruction one slot behind it can't be served by any
bypass. It waits one cycle. The violet cells are held — the program
counter and the fetch register freeze, and a bubble goes into execute.
One cycle is always enough, because by then the load is in write-back
and the second forwarding path works.
[RIGHT] Control hazards. A conditional branch resolves in execute, so
by the time we know it's taken, two instructions behind it have
already been fetched. Both are killed. They never write a register,
never write memory, and never count as retired.
[RIGHT] Costs on the strip: one cycle for a load-use, one bubble for
jal, two for a taken branch or a jalr, two for a trap or an mret.
And one rule that's easy to get wrong: a redirect always overrides a
stall. The instruction that raised the stall is being killed anyway,
so waiting for it would deadlock the redirect.

## Slide 12
02 · Implementation
IF
ID
EX
MEM
WB
12 / 20
BONUS A — BRANCH PREDICTION
64 two-bit counters, and an honest cost table
00
strongly not taken
taken
not taken
01
weakly not taken
taken
not taken
10
weakly taken
taken
not taken
11
strongly taken
predict NOT TAKEN
predict TAKEN
reset state
64 entries
index pc[7:2]
untagged
prediction = state[1]
WHAT IT COSTS, BY OUTCOME
Prediction
Outcome
Bubbles
Why
not taken
not taken
0
the fall-through was already being fetched
taken
taken
1
the ID redirect kills one instruction
not taken
taken
2
EX redirect kills ID and IF
taken
not taken
2
wrong target fetched, then re-fetch
WHERE EACH STEP HAPPENS
LOOKUP — IF
indexed by the fetch PC, in parallel with the fetch
CARRY — IF/ID
the counter state travels with the instruction
ACT — ID
redirect to PC + immB, the 1-bubble path jal uses
RESOLVE — EX
compare with the real outcome; flush 2 on a mispredict
UPDATE — EX
saturating increment or decrement
There is no target buffer. The target is PC + immB, which ID already computes. That saves a tagged CAM and costs one bubble on a correct taken prediction.
Notes: First bonus. Sixty-four entries of two-bit saturating counters,
indexed by bits two to seven of the PC.
The state machine is standard. Taken moves right, not-taken moves
left, both ends saturate, and the prediction is just the top bit. We
reset to weakly-not-taken, so a branch we've never seen behaves
exactly like the machine with no predictor.
[RIGHT] Now the honest part — the cost table.
Predict not-taken and it isn't taken: zero bubbles, because the fall-
through was already being fetched. Predict taken and it is taken: ONE
bubble, not zero. A mispredict in either direction: two.
That one-bubble cost is real and we don't hide it. There's no branch
target buffer, because the target is just PC plus the branch immediate
and decode already computes it. Dropping the target buffer saves a
tagged memory and costs one cycle on a correct prediction.
[RIGHT] So: looked up in fetch, carried through the pipeline register,
acted on in decode, resolved and updated in execute.
Which means this predictor can only win on branches that are actually
taken. A correctly predicted not-taken branch already cost nothing.

## Slide 13
02 · Implementation
IF
ID
EX
MEM
WB
13 / 20
BONUS B — INTERRUPTS
The trap point is EX, so mepc is always a real PC
c1
c2
c3
c4
c5
c6
c7
I(n−2)
EX
MEM
WB
retires normally
I(n−1)
ID
EX
MEM
WB
retires normally
I(n)
IF
ID
EX
X
SQUASHED — never retires, never traced
I(n+1)
IF
ID
X
killed
I(n+2)
IF
X
killed
ISR[0]
IF
ID
EX
MEM
handler at mtvec
irq sampled with a valid instruction in EX
mepc ← PC of I(n) · mcause ← 0x8000000B · MPIE ← MIE, MIE ← 0 · PC ← mtvec
ECALL — SYNCHRONOUS
mcause = 11. mepc points at the ecall, which has not completed. The handler must add 4 before mret.
INTERRUPT — ASYNCHRONOUS
mcause = 0x8000000B. mepc points at an instruction that never executed. The handler must not add 4. mret re-runs it.
LEVEL, NOT PULSE
irq is qualified by mstatus.MIE and mie.MEIE. A request raised inside the handler is held, not lost, and taken when mret restores MIE.
That asymmetry, ecall advances mepc and an interrupt must not, is the single most common trap-handling bug.
Notes: Second bonus. Machine-mode interrupts with the minimum CSR set:
mstatus, mie, mtvec, mepc and mcause, the six CSR instructions, and
mret.
[STEP 1] The trap is taken in execute, and this timeline shows why
that matters. The instruction in execute when the interrupt arrives is
SQUASHED — it never retires and never appears in the commit trace. The
two behind it are killed. The two ahead are already past execute, so
they do retire.
[RIGHT] At that point mepc gets the PC of the squashed instruction,
mcause gets the external interrupt code, the enable bit is saved into
MPIE and cleared, and the PC goes to mtvec.
[RIGHT] Now the detail I'd most like you to take away, because it's
the classic trap-handling bug.
On an ecall, mepc points AT the ecall, which hasn't completed. The
handler MUST add four before returning, or it re-executes forever.
On an interrupt, mepc points at an instruction that NEVER EXECUTED.
The handler must NOT add four — mret re-runs it. Same register,
opposite rule.
Last thing: the interrupt input is a level, not a pulse, and it's
qualified by the enable bits. So a request arriving while the handler
runs isn't lost. It's taken as soon as mret restores the enable.

## Slide 14
02 · Implementation
IF
ID
EX
MEM
WB
14 / 20
SYNTHESIS — VIVADO 2026.1, xc7a35tcpg236-1, POST PLACE-AND-ROUTE
Setup timing met at 74 MHz
1,461
LUTs
7.0 % of the device
819
flip-flops
2.0 % of the device
2
block RAMs
IMEM + DMEM, 4 % of 50
44
LUTs as memory
the 32x32 register file
CONSTRAINT SWEEP — WHERE IT CLOSES
Configuration
Period
WNS
Failing
Result
base machine
10.0 ns
−2.483
423
not met
full design
10.0 ns
−3.235
555
not met
full design
12.5 ns
−0.755
306
not met
full design
13.5 ns
+0.052
0
met — 74 MHz
The three points agree to within 1.6 % on 1/(T − WNS). The speed is a property of the design, not of the constraint. Register-to-register hold is met at every point.
CRITICAL PATH — A LOAD FEEDING A BRANCH
DMEM block RAM
clock to output
2.454 ns
byte-lane select
+ sign extension
in WB · 2 x LUT6
MEM/WB to EX
forwarding mux
load into a branch
branch comparator
branch_unit.v
3 x CARRY4
redirect / flush
reduction
PC register
clock enable
endpoint
12.982 ns total 15 logic levels 65 % routing Fixes designed: register the lane extension into WB · precompute the forwarding match bits in ID
74 MHz is measured, not estimated, and the path that limits it is identified. That makes the two planned fixes a scheduled task rather than a hope.
Notes: Synthesis, on an Artix-7, placed and routed.
Fourteen hundred and sixty-one LUTs, eight hundred and nineteen flip-
flops, two block RAMs. About seven percent of the device.
[RIGHT] The sweep. At ten nanoseconds we're three short. At twelve and
a half still slightly short. At thirteen and a half we close, with
positive slack and zero failing endpoints. Seventy-four megahertz. The
figure is consistent across all three points to about one percent,
which is the useful check — it's a property of the design, not of the
constraint we asked for.
[RIGHT] The critical path is a load feeding a branch. The block RAM
output alone is two and a half nanoseconds. Then lane extension in
write-back, the forwarding mux, the branch comparator, and the
redirect into the program counter's enable.
Seventy-four megahertz is measured, not estimated, and we know exactly
what limits it. That's what makes the two fixes a scheduled task
rather than a hope.
[Name] will show you how all of this is verified.

## Slide 15
03 · Verification
IF
ID
EX
MEM
WB
15 / 20
SPEAKER 3 OF 3 · [ 王伟成 ]
Testing — proving it, and measuring it
Nothing here is judged by looking at a waveform. Every test states its own verdict, and every golden value comes from the reference model rather than from a person.
OWNED END TO END
PLAN
The three-tier strategy and the pass criteria for each tier
UNIT
A testbench for every module that is not pure wiring
PROGRAMS
One program per encoding, plus nine directed hazard programs
DIFFING
The RTL-versus-reference trace harness and the regression driver
MEASUREMENT
CPI with forwarding on and off, predictor accuracy, synthesis reporting
DEMO
The demo script and the evidence captures for the final presentation
26,447
unit vectors
11 testbenches
68
programs
run at 4 configs
0
trace diffs
against the ISS
DELIVERED
• 11 unit testbenches totalling 26,447 vectors
• 68 assembly programs and the trace-diff harness
• Mutation checks: every testbench shown to FAIL against a broken module
WHERE TO LOOK
Green at all four FORWARDING × BHT_ENABLE configurations, byte-exact against the reference model.
A test that has never been shown to fail is not yet evidence. That is why the mutation checks exist.
Notes: Thanks. My job is to prove the thing works, and then to measure it.
The principle I'd lead with: nothing in this project is judged by
looking at a waveform. Every test states its own verdict — it prints
PASS or FAIL and exits with a code the script checks. And every
expected value comes from the reference model, not from a person
typing what they think the answer should be.
That second point is the one that matters. If I hand-wrote the golden
values, I'd be checking the RTL against my own understanding of the
spec — which is the same understanding that might be wrong.
Headline numbers: twenty-six thousand unit-level vectors across eleven
testbenches, sixty-eight assembly programs, and zero differing trace
lines against the reference model.

## Slide 16
03 · Verification
IF
ID
EX
MEM
WB
16 / 20
STRATEGY
Three tiers, and nothing checked by eye
TIER 3 — DIFFERENTIAL TESTING
A second, independent implementation of the same instruction set, written in Python without reference to the Verilog.
Both execute the same image and emit the same commit-trace format. The files are diffed line by line, so a mismatch names the exact retiring instruction.
iss.py
TIER 2 — SELF-CHECKING TESTS
A standalone testbench for every module that is not pure wiring, plus one assembly program per encoding with golden state.
Every vector is generated by the already cross-validated tools, never by a second hand-written copy of the logic being tested.
11 + 46
TIER 1 — THE BATCH FLOW
Every simulation runs through the same three commands in batch mode: no GUI, no waveform viewer, no human judgement in the loop.
A run exits zero only if the log contains a PASS line and no FAIL line, so a regression cannot pass by being ignored.
xvlog / xelab / xsim
The commit trace is <pc> <insn> x<rd>=<value> mem[<addr>]=<value> — the same line from the RTL write-back stage and from the reference model.
A trace diff localises a bug to one retiring instruction. For a five-stage pipeline that is an afternoon of debugging instead of a week.
Notes: Three tiers.
[STEP 1] Tier one is the flow. Every simulation goes through the same
three commands in batch mode. No GUI, no waveform viewer, nobody
deciding by eye. A run exits zero only if the log has a PASS line and
no FAIL line, so a regression can't quietly pass by being ignored.
[RIGHT] Tier two is the self-checking tests. A standalone testbench
for every module that isn't just wiring, plus one assembly program per
instruction with a golden register file. Every vector is generated by
the tools we'd already cross-validated — never by a second hand-
written copy of the logic I'm testing.
[RIGHT] Tier three is differential testing, and it's the strongest
thing we have. The reference model is an independent implementation of
the same instruction set, written in Python without reference to the
Verilog. Both run the same image. Both print one line per retiring
instruction. Then we diff the files.
Why that's worth the effort: a final-state check tells you the answer
is wrong. A trace diff tells you WHICH INSTRUCTION went wrong. On a
five-stage pipeline that's the difference between an afternoon and a
week.

## Slide 17
03 · Verification
IF
ID
EX
MEM
WB
17 / 20
RESULTS
Green at every build configuration
26,447
unit-level vectors
across 11 testbenches
4,323
toolchain checks
assembler vs reference
68
assembly programs
46 + 9 + 5 + 7 + 1
4
build configurations
forwarding x predictor
THE FIVE LARGEST SUITES
Suite
Count
What it proves
tb_branch_unit
16,072
all six conditions, signed and unsigned
tb_alu
5,072
11 operations, every shift amount
tb_bht
2,600
saturation, aliasing, same-cycle access
tb_imm_gen
1,865
all six immediate formats and their traps
tb_control
667
the full truth table, 120 illegal encodings
This suite is the acceptance criterion from slide 2, already running. Golden values come from the reference model, never from a person, so a test cannot agree with the RTL by accident.
Notes: The results.
Twenty-six thousand four hundred unit vectors. Four thousand three
hundred toolchain checks — the assembler against the reference model,
before any RTL is involved. Sixty-eight assembly programs. And all of
it runs at four build configurations: forwarding on and off, predictor
on and off.
The biggest suites are on the left. The branch unit alone is sixteen
thousand vectors. The control decoder is six hundred and sixty-seven,
including a hundred and twenty deliberately illegal encodings.
[RIGHT] (point at the screenshot) And that's the regression output
itself, so you can see these came out of a tool rather than a table I
typed.
This suite is the acceptance criterion from slide two, already
running.

## Slide 18
03 · Verification
IF
ID
EX
MEM
WB
18 / 20
PERFORMANCE
The same three programs finish in 6,799 cycles instead of 9,003
0
0.6
1.2
1.8
2.4
ideal CPI = 1.0
1.368
2.263
fib
1.65x faster
1.376
1.904
bsort
1.38x
1.396
1.707
bloop
1.22x
forwarding on
forwarding off, stall instead
CYCLES PER INSTRUCTION — FORWARDING ON vs OFF
CHANGE IN CYCLE COUNT WITH THE PREDICTOR ON
0 %
-10
-5
+5
+10
-14.5 %
bpred
95.5 % accurate
-8.8 %
fib
93.4 % accurate
+0.5 %
bsort
75.3 % accurate
+10.0 %
bloop
49.9 % — adversarial
cycles saved
cycles cost
READING BOTH CHARTS
Forwarding helps most where dependencies are tight. fib gains 1.65x; bloop's load-use stall count is zero even with forwarding on, so there was nothing to save.
The predictor can only win on taken branches. bloop was written to defeat a 2-bit counter, and the 400-cycle loss matches the arithmetic exactly.
Slide 2 promised performance measured against a baseline rather than quoted in isolation. This is that measurement, for both bonus features.
Notes: Performance. Slide two promised we'd measure this against a baseline
rather than quote it in isolation. This is that measurement.
[STEP 1] First, forwarding. A compile-time parameter disables the
entire bypass network, and correctness is restored by stalling
instead. Same programs, same predictor setting, one parameter changes.
The three benchmarks together run in six thousand seven hundred and
ninety-nine cycles with forwarding, and nine thousand and three
without. One point three two times.
Per program: Fibonacci gains most, one point six five, because its
inner loop is a tight dependent chain — every iteration consumes the
previous result almost immediately. The branch loop gains least, one
point two two, and why is interesting: its load-use stall count is
zero even with forwarding on, because its loop bodies compute
independent things. There was nothing for the bypass network to save.
The dashed line is CPI of one. Everything above it, with forwarding
on, is control-flow bubbles and load-use stalls. No other source of
delay in this design.
[RIGHT] Second, the predictor. This is the change in cycle count when
we turn it on. Left is saved, right is cost.
The prediction demo saves fourteen and a half percent at ninety-five
percent accuracy. Fibonacci saves nearly nine.
But the branch loop gets ten percent WORSE, and we're showing you that
deliberately. That program was written to defeat a two-bit predictor —
its inner branch tests whether a counter is odd, so it alternates on
every iteration. That's the one pattern a saturating counter cannot
learn. The loss works out to exactly four hundred cycles, and the
measurement is exactly four hundred.
[RIGHT] So the honest summary: a two-bit table helps loop-dominated
code, does nothing for exit-dominated code, and hurts on alternating
branches. A cheap heuristic, not a guarantee. And correctness never
depends on it — with the predictor off, the machine reproduces the
static cycle counts exactly.

## Slide 19
03 · Verification
IF
ID
EX
MEM
WB
19 / 20
SIMULATION EVIDENCE
The hazard logic, seen in the waveform
WHAT THE AUDIENCE SHOULD SEE
STALL HIGH
for exactly one cycle, while ex_valid drops — the pipeline bubble
FWD_A / FWD_B
switching to 01 the cycle after, the MEM/WB bypass delivering the load
FLUSH_IF / ID
shown alongside, redirecting the front of the pipe on a taken branch
TRACE_VALID
dropping for the squashed slot inside the bubble
WHY THIS SLIDE EXISTS
The course task asks us to use the simulation tools to show the function of the CPU. The PASS lines prove it to a machine. This is the picture that proves it to a person.
Correctness is decided by the self-checking testbenches, never by reading a waveform. The waveform is evidence for the audience, not the test.
Notes: One piece of evidence that isn't a number.
(point at the waveform) This is the load-use case in the simulator.
The stall signal goes high for exactly one cycle, and while it does,
the program counter and the fetch register hold their values. The
cycle after, the forwarding select switches to the Memory-Writeback
path — the bypass delivering the loaded value.
[RIGHT] Further along, flush on the fetch and decode registers pulsing
together on a taken branch, killing two slots, and the trace-valid
signal never asserting for either.
I want to be precise about what this slide is. Correctness is decided
by the self-checking testbenches, never by reading a waveform. This is
evidence for you, not the test.

## Slide 20
Summary
IF
ID
EX
MEM
WB
20 / 20
WHERE WE ARE
What we are committing to, and why we can
FUNCTION
46 encodings execute correctly on a 5-stage pipeline with full forwarding, a load-use interlock and flush-based control recovery.
Checked against an independent reference model, byte for byte, at every build configuration.
PERFORMANCE
Forwarding is worth 1.32x overall and 1.65x on the tightest dependent loop. The predictor reaches 95.5 % where branches are taken.
Both measured by counters in the RTL, both with the feature switched off as the baseline.
BETWEEN HERE AND SEP 17
Two timing improvements, the final regression on the frozen RTL, the final synthesis run, and the demo package.
None of it is new design work. It is finishing measurement on a machine that already runs.
IF
ID
EX
MEM
WB
Every criterion on slide 2 is already met once. What remains is measurement on a machine that runs, not design.
Notes: To close.
Function: forty-six encodings execute correctly on a five-stage
pipeline with full forwarding, an interlock and flush-based recovery,
checked byte for byte against an independent model at every build
configuration.
Performance: forwarding is worth one point three two times overall,
one point six five on the tightest loop, and the predictor reaches
ninety-five percent where branches are taken. Both measured with the
feature switched off as the baseline.
Between here and the seventeenth: two timing improvements, the final
regression, the final synthesis run, and the demo package.
Every criterion we set on slide two is already met once. What remains
is measurement on a machine that runs, not design work.
Thank you — happy to take questions.

## Slide 21
Appendix — if asked
IF
ID
EX
MEM
WB
A1
APPENDIX
Design decisions, and what each one cost
ARCHITECTURE
ISA
RV32I user subset plus simplified machine-mode CSRs
PIPELINE
5 stages, in-order issue, in-order completion
MEMORY
Harvard, 4 KB + 4 KB, single-cycle synchronous
RESET
Synchronous, active high, PC to 0x00000000
HAZARDS AND CONTROL FLOW
DATA
Full EX/MEM and MEM/WB forwarding; EX/MEM has priority; x0 never forwarded
LOAD-USE
1-cycle interlock, then served by the MEM/WB bypass
JAL / BRANCH
ID, 1 bubble / EX, 2 bubbles
BASELINE
FORWARDING disables the bypass network for the CPI comparison
BONUS SCOPE
BRANCH PRED.
Implemented, 64-entry 2-bit BHT with accuracy counters
INTERRUPTS
Implemented, mstatus / mie / mtvec / mepc / mcause, CSR instructions, mret, external irq
I-CACHE
Cut on purpose. Behind a single-cycle memory a hit and a miss cost the same, and the suite fits in 2 KB, so the hit rate would read ~99 % and prove nothing
TOOLCHAIN AND TARGET
HDL
Plain synthesizable Verilog-2001, no IP catalog, no block design
SIMULATOR
Vivado 2026.1 xsim, batch flow
REFERENCE
Written in Python. Mars4_5 is MIPS-only and cannot execute RISC-V
PART
xc7a35tcpg236-1, simulation plus synthesis report, no board
Cutting the cache was a measurement decision, not a schedule one.

## Slide 22
Appendix — if asked
IF
ID
EX
MEM
WB
A2
APPENDIX
19 RTL modules, and the two tools we wrote first
rtl/ — 19 MODULES, PLAIN VERILOG-2001
PIPELINE REGISTERS — 4
if_id.v
id_ex.v
ex_mem.v
mem_wb.v
DATAPATH — 7
pc.v
regfile.v
alu.v
alu_ctrl.v
imm_gen.v
control.v
branch_unit.v
HAZARD LOGIC — 2
forward_unit.v
hazard_unit.v
BONUS AND INSTRUMENTATION — 3
bht.v
csr.v
perf_counters.v
MEMORY AND TOP — 3
imem.v
dmem.v
cpu_top.v
tools/ — THE TOOLCHAIN PROBLEM
The course names Mars4_5 as the simulator. Mars executes MIPS, not RISC-V, so there was no reference model to check the RTL against. We wrote one.
program.s
asm.py
program.hex
iss.py
cpu_top · xsim
diff
861
lines of assembler
two-pass, 6 formats
589
lines of ISS
emits the commit trace
Building our own reference model forced every ISA question to be answered once, explicitly, before the RTL was written.

## Slide 23
Appendix — if asked
IF
ID
EX
MEM
WB
A3
APPENDIX
How we know the tests would actually fail
MUTATION CHECKS — A BROKEN MODULE MUST PRODUCE FAIL
Bug injected on purpose
Caught by
SRA as a logical shift
tb_alu, negative-operand vectors
WB to ID bypass removed
tb_regfile
B-format immediate bit flipped
tb_imm_gen
alu_ctrl reads inst[30] for addi
tb_control, the addi / sub trap
Forwarding priority swapped
asm/hazard/fwd_ex_ex.s
x0 guard removed from forwarding
asm/hazard/x0_hazard.s
Load-use interlock disabled
asm/hazard/load_use.s
lb sign extension removed
tb_dmem and asm/insn/lb.s
BHT trained with the inverted outcome
nothing, and that is correct
THE LAST ROW IS THE INTERESTING ONE
Training the predictor with the inverted outcome collapses accuracy. fib falls from 93.4 % to 3.3 %, and bloop costs another 438 cycles.
Yet every program still passes its byte-exact trace diff.
That is the right answer. The predictor only changes when instructions are fetched, never what they compute. Correctness rests entirely on the EX-stage resolution and flush, and the trace diff should be blind to a misprediction rate.
A testbench is not trusted until it has been shown to fail against a deliberately broken copy of the module it checks.